SciPhi – The road to the top500
‌‌Kurt J. Strosahl (strosahl@jlab.org)
System Administrator: Lustre, HPC
Scientific Computing Group, Thomas Jefferson National Accelerator Facility

---
Thomas Jefferson National Accelerator Facility (JLAB)
- Continuous Electron Beam Accelerator Facility
- Not a Physicist
- Scientific Computing group
  - Long term data storage for data produced by the accelerator
  - Provide computing power to process the data to physicists working with the lab and the LQCD (lattice quantum chromodynamic) project.

---
What metric does the top500 use
- FLOPS: Floating-point Operations Per Second
- Measured using the Linpack benchmark
- Our system reached 425.9 TFLOPS/s with 16,896 cores, ranked 397

---
Knights Landing (KNL) Xeon Phi
Multi Integrated Cores (MIC), first released in 2011
  - Each core is individually slower, with performance coming from code parallelization
- 16GB MCDRAM on-chip
- x86 architecture
- Configurable
  - MCDRAM usage
    - Cache / flat
  - Cores
    - Quad / All2All
~> lscpu
Architecture:          x86_64
CPU op-mode(s):        32-bit, 64-bit
Byte Order:            Little Endian
CPU(s):                256
On-line CPU(s) list:   0-255
Thread(s) per core:    4
Core(s) per socket:    64
Socket(s):             1
NUMA node(s):          1
Vendor ID:             GenuineIntel
CPU family:            6
Model:                 87
Model name:            Intel(R) Xeon Phi(TM) CPU 7230 @ 1.30GHz
Stepping:              1
CPU MHz:               1404.101
BogoMIPS:              2594.02
L1d cache:             32K
L1i cache:             32K
L2 cache:              1024K
NUMA node0 CPU(s):     0-255

---
KNL cont

---
The Compute node
In addition to the Xeon Phi processor each of the 264 compute nodes has the following:
  - Intel Omnipath Architecture connection
    - 4 channels at 25 Gb/s speed giving a total of 100 Gb/s
    - Comparable to EDR Infiniband
  - Intel Motherboard, providing direct access to OPA interface
  - 192GB of RAM
  - 1TB Hard disk
  - Runs CentOS 7.2 with a custom kernel provided by Intel
  - Is a blade in a chassis of 4 nodes.

---
Building the cluster
- Physical installation provided by vendor (Koi Computing)
- Basic Build on a test system (install OS, basic network configuration)
- Work with Intel support to get correct kernel, drivers, bios
- Configure a single compute node.
  - Network drivers, configuration
  - Kernel and software (xppsl stack)
Use configuration management software to build entire cluster
  - We used the Salt Stack, but any CM software can do it.

---
GPUs, the competition
- Provide custom hardware for performing matrix operations
- Are very fast, for certain types of problems
- Have a high power consumption, and a high heat output
- Require specialized code (CUDA)

---
Production Use
- System shared among a number of different projects (torque PBS and Maui scheduler manages)
- Users have access to a compiler suite from Intel with advanced debugging and optimization tools
- System has access to a 2.3PB file system to enable transfer and storage of large data sets
- Has had near 100% utilization since going into production in October

---
Issues encountered
The build is more complicated than other builds
  - Requires installation of kernel, rebooting, than installation of opa software
- On chip memory (MCDRAM) seems to have higher than expected rates of failure (12 nodes so far).
- Initial BIOS did not regulate the fans, instead running them at max speed at all times.
  - Cluster was very noisy
  - BIOS update resolved this issue
  - Update of BIOS was done using Intel provided tool that allowed patching to be done via script submitted through the scheduler

---
Questions?